## Slide 1
Using TerriaMap (CSIRO) with GSKY (NCI)
NATIONAL MAP
“TerriaJS was born late 2014 thanks to NationalMap. It started as a web based platform. The Australian NationalMap platform contributed greatly in opening data by government agencies and in discovering and consuming open data by general public, industry, academia and the government itself. NationalMap is managed and maintained by: Digital Transformation Agency - product ownership, Geoscience Australia - product hosting, Data61 Terria - product software development.”[Ref]
Next slide is a non-technical user guide.
Three slides that follow it will show the process with code snippets.
GSKY_OWS_Server.docx for details.
It will take approximately 8 minutes to watch this animation.
Use GSKY_Terria_Interaction.pptx for controlled slideshow at your own pace.
The slide show will begin in 5 seconds !
DISCLAIMER
Only some relevant code snippets from TerriaMap (TerriaJS-specs.js) and GSKY (ows.go) are shown. They give pointers to understand the programs by studying the full codes. It is out of scope to include all code. More details are given in the above Word document. Gaps exist in code descriptions and the information may change over time.
1

## Slide 2
This animation will demonstrate the use of GSKY through TerriaMap, using the GEOGLAM data. There are more layers than those shown here, but not all may have displayable data. In some cases you will have to zoom in to see any overlaid data.
Add data
TerriaMap/GSKY User Guide
1. Click: Add data
2. Click: My data
3. Click: Add Web Data
4. Type: Address of GSKY server. Click: Add
5. Click: A layer name
6. Click: Add to the map
7. Zoom: Use the mouse wheel
8. Click: On any pixel on the map
Next: Technical Details
My Data
Add Web Data
Add
http://130.56.242.15/ows/geoglam
GEOGLAM Anomaly Fractional Cover C6
Add to the map
2

## Slide 3
This is an overview of the calls from TerriaMap to GSKY and the return communications. TerriaMap calls GSKY to get the relevant information and displays them over the map. There are five request-types, viz. GetCapabilities, DescribeLayer, GetLegendGraphic, GetMap and GetFeatureInfo. These are called sequentially.
GSKY
GetCapabilities
XML:WMS_GetCapabilities.tpl
Service: Name, Title, Abstract, Keywords, ContactInformation
Capability: DCPType, FeatureInfo, Exception
Layers: Title, Abstract, Bbox, CRS, Times, MetadataURL, DataURL
DescribeLayer
WMS_DescribeLayer.tpl <WMS_DescribeLayerResponse version="1.1.1">
<LayerDescription name="global:c6:monthly_anom_frac_cover" owsURL="http://130.56.242.15/ows/geoglam" owsType="WMS">
<Query typeName="global:c6:monthly_anom_frac_cover"/>
</LayerDescription>
</WMS_DescribeLayerResponse>
GetLegendGraphic
WMS_ServiceException.tpl <ServiceExceptionReport version="1.1.1" >
<ServiceException code="LayerNotDefined" locator="MapLayerInfoKvpParser">{{ . }} no such layer on this server.</ServiceException>
</ServiceExceptionReport>
GetMap
case "GetMap": &proc.GeoTileRequest{ConfigPayLoad: proc.ConfigPayLoad{… proc.NewTileIndexer(ctx, conf.ServiceConfig.MASAddress, errChan) go indexer.Run(*verbose) proc.InitTilePipeline(…) tp.Process(geoReq, *verbose): tils.EncodePNG(norm, styleLayer.Palette) w.Write(out)
Next: Process flow at code level
GetFeatureInfo
case "GetFeatureInfo":
type:FeatureCollection
Properties: x, y, time, feat_info
TerriaMap/GSKY Communication
3

## Slide 4
Geo-spatial data stored in GSKY database can be layered over a world map. Steps and code snippets to show the usage and inner workings.
GEOGLAM – An implementation via GSKY in TerriaJS
gopath/src/github.com/nci/gsky/ows.go:179: case GetCapabilities:
utils.ExecuteWriteTemplateFile(w, conf, utils.DataDir+"/templates/WMS_GetCapabilities.tpl")
http://130.56.242.15/ows/geoglam?service=WMS&request=GetCapabilities&version=1.3.0&tiled=true
/TerriaMap/build/TerriaJS/build/TerriaJS-specs.js:44818:
layerTitles: {
get: function get() {
return this._allLayersInRawMetadata.map(function (layer) {
return layer.Title || layer.Name;
});
}
}
Next Slide
Add data
My Data
Add Web Data
Add
Add to the map
GEOGLAM Anomaly Fractional Cover C6
/TerriaMap/build/TerriaJS/build/TerriaJS-specs.js:44667:
return cleanUrl(this.url) + '?service=WMS&version=1.3.0&request=GetCapabilities';

## Slide 5
TerriaJS is a Node.JS implementation of a webserver that can connect to various data sources that comply with WMS formats. It can send requests to GSKY and display the returned results. This slide will show an overview of the process flow. Code snippets from both TerriaJS and GSKY are shown.
http://130.56.242.15/ows/geoglam?time=2001-01-01T00%3A00%3A00.000Z&srs=EPSG%3A3857&transparent=true&format=image%2Fpng&exceptions=application%2Fvnd.ogc.se_xml&styles=&tiled=true&feature_count=101&service=WMS&version=1.1.1&request=GetMap&layers=global%3Ac6%3Amonthly_anom_frac_cover&bbox=15028131.257091936%2C-5009377.085697312%2C17532819.79994059%2C-2504688.542848654&width=256&height=256
http://130.56.242.15/ows/geoglam?time=2001-01-01T00%3A00%3A00.000Z&srs=EPSG%3A3857&transparent=true&format=image%2Fpng&exceptions=application%2Fvnd.ogc.se_xml&styles=&tiled=true&feature_count=101&service=WMS&version=1.1.1&request=GetMap&layers=global%3Ac6%3Amonthly_anom_frac_cover&bbox=15028131.257091936%2C-2504688.542848654%2C17532819.79994059%2C0&width=256&height=256
http://130.56.242.15/ows/geoglam?time=2001-01-01T00%3A00%3A00.000Z&srs=EPSG%3A3857&transparent=true&format=image%2Fpng&exceptions=application%2Fvnd.ogc.se_xml&styles=&tiled=true&feature_count=101&service=WMS&version=1.1.1&request=GetMap&layers=global%3Ac6%3Amonthly_anom_frac_cover&bbox=12523442.714243278%2C-2504688.542848654%2C15028131.257091936%2C0&width=256&height=256
http://130.56.242.15/ows/geoglam?time=2001-01-01T00%3A00%3A00.000Z&srs=EPSG%3A3857&transparent=true&format=image%2Fpng&exceptions=application%2Fvnd.ogc.se_xml&styles=&tiled=true&feature_count=101&service=WMS&version=1.1.1&request=GetMap&layers=global%3Ac6%3Amonthly_anom_frac_cover&bbox=15028131.257091936%2C-5009377.085697312%2C17532819.79994059%2C-2504688.542848654&width=256&height=256
GEOGLAM – An implementation via GSKY in TerriaJS
/TerriaMap/build/TerriaJS/build/TerriaJS-specs.js:45977:
legendUri = new URI(cleanUrl(catalogItem.url) + '?service=WMS&version=1.1.0&request=GetLegendGraphic&format=image/png&transparent=True&layer=' + encodeURIComponent(thisLayer.Name));
http://130.56.242.15/ows/geoglam?service=WMS&version=1.1.0&request=GetLegendGraphic&format=image%2Fpng&transparent=True&layer=global%3Ac6%3Amonthly_anom_frac_cover&srs=EPSG%3A3857
/TerriaMap/build/TerriaJS/build/TerriaJS-specs.js:45449:
return new WebMapServiceImageryProvider({
url: cleanAndProxyUrl(this, this.url),
layers: this.layers,
getFeatureInfoFormats: this.getFeatureInfoFormats,
parameters: parameters,
getFeatureInfoParameters: parameters,
tilingScheme: defined(this.tilingScheme) ? this.tilingScheme : new WebMercatorTilingScheme(),
maximumLevel: maximumLevel
});
gopath/src/github.com/nci/gsky/ows.go:220::
case GetMap:
proc.InitTilePipeline(ctx, conf.ServiceConfig.MASAddress, conf.ServiceConfig.WorkerNodes, conf.Layers[idx].MaxGrpcRecvMsgSize, conf.Layers[idx].WmsPolygonShardConcLimit, conf.ServiceConfig.MaxGrpcBufferSize, errChan)
out, err := utils.EncodePNG(norm, styleLayer.Palette)
w.Write(out)
gopath/src/github.com/nci/gsky/ows.go:206:
case DescribeLayer:
utils.ExecuteWriteTemplateFile(w, conf.Layers[idx], utils.DataDir+"/templates/WMS_DescribeLayer.tpl")
/TerriaMap/build/TerriaJS/build/TerriaJS-specs.js:45298:
var describeLayersURL = cleanUrl(that.url) + '?service=WMS&version=1.1.1&sld_version=1.1.0&request=DescribeLayer&layers=' + encodeURIComponent(that.layers);
http://130.56.242.15/ows/geoglam?service=WMS&version=1.1.1&sld_version=1.1.0&request=DescribeLayer&layers=global%3Ac6%3Amonthly_anom_frac_cover
5
End of the slide show !