## Slide 1: QGIS Desktop Tutorial
Installation of QGIS 3.4.x
Use QGIS as a GSKY client
Advanced usage of QGIS
Copyright © 2019 by National Computational Infrastructure, Canberra, ACT, Australia. Author: Arapaut V. Sivaprasad.
Jan 10, 2019
This presentation must be viewed as a slide show

## Slide 2
Introduction to QGIS and Technical Specifications.
Install and configure a desktop version.
Use QGIS as a GSKY client.
Advanced usage of QGIS.
SUMMARY
In this tutorial we address the following:
Slides 3 - 7 describe the use of QGIS as GSKY client.
Slides 8 - 12 describe the advanced usage of QGIS.
Animated slides that follow will describe the usage stop-by-step. It is important to run as a slideshow to see the full picture.
Slide show will start in 5 sec.
NOTE:
This slide show is a quick way to learn the basic usage of QGIS in relation to using it as a GSKY client. The intention is to reduce the learning time from several hours to a few minutes, but it will not make you an expert in the use of QGIS or GSKY through QGIS. For those who wish to learn deeper, see the Word/PDF documents that give both pictorial and textual description of all that in this slide show and more.

## Slide 3
Introduction to QGIS
QGIS is a Free and user friendly Open Source Geographic Information System (GIS) licensed under the GNU General Public License. QGIS is an official project of the Open Source Geospatial Foundation (OSGeo). It runs on Linux, Unix, Mac OSX, Windows and Android and supports numerous vector, raster, and database formats and functionalities. The latest release is QGIS 3.4 [Ref]
In this tutorial we plan to explore the installation of QGIS 3.4.x, its basic usage and the use of QGIS as a GSKY client.
The last released older version of QGIS, probably deprecated soon, is 2.18.28.
The one integrated into NCI’s VDI is v 2.14.8. There are problems with the older versions to use them as GSKY clients.
TECHNICAL
[Ref]
QGIS is developed using the Qt toolkit and C++.
QGIS supports a number of raster , vector and mesh data formats, with new support easily added using the plugin architecture.
Read more about QGIS and the supported data formats.
Clone the GitHub Repo
https://download.qgis.org/
Download QGIS for your platform. Binary packages (installers)
Next: First and/or Clean Installation

## Slide 4
Download and Install
Download the installation package
  - Double click the saved file.
Next: Configure the Project Properties
2. Launch the software
TIP: For a clean start, delete the cache and previous settings, if any. This is useful if you re-install QGIS. It can be done at any time to discard previously cached images and settings for a clean start.
Delete or rename this dir: C:\Users\userID\AppData\Roaming\QGIS

## Slide 5
Configure Project Properties
Next: Add a Base Map
This step is required only once after a clean installation.
1. Choose Project | Properties from top menu and click CRS.
2. Type in 3857 in ‘Filter’
3. Click ‘WGS 84 / Pseudo-Mercator’ and click Apply/OK.
This step is important for GSKY layers to work properly.
4. Set the view panels

## Slide 6
Add a Base Map
Next: Add GSKY Map Services
A basic street map is included by default, which is all that you require. Fancy maps can be installed as plugins. Most of them will require API Keys from their providers.
Show the OpenStreetMap Layer:
  - Double click “OpenStreetMap”
Add Quick Map Services
Change a base map

## Slide 7
Add GSKY Map Services
Next: Advanced Usage of QGIS
In this step we will add the WMS layers to implement the GSKY service.
For demonstration, the GEOGLAM and DEA Landsat8 layers are added through the GSKY Map Service.
Add the WMS Layer(s)
You may close without adding
Display layers(s)
  Double click the layer name
  Drag to top in layers’ list.

## Slide 8
Advanced Usage of QGIS
Next: Download OSM Data
QGIS has several options and settings to configure the way layers are displayed. This section gives an introduction to some that are useful in GSKY services. It is by no means a comprehensive list. Some demonstrations are currently not available with the GSKY service, but may be added later.
Here we demonstrate the following:
  Adding OSM Data
  Adding publicly available layers in OSM
  Configuring layer properties
  Scale-based visibility (useful in GSKY)
  Attribute Data and Labelling (not available in GSKY)

## Slide 9
Download OSM Data
QuickOSM is a plugin that allows you to find and download data layers corresponding to a large variety of things such as water ways, roads, land use, buildings, public transport and many more. You must be zoomed into an area that has data corresponding to the layer to be added. For example, zooming to the centre of Australia and asking to add buildings layer will return empty. [Ref]
STEPS
Install the QuickOSM plug-in
  Plugins | Manage and Install Plugins
  All | Search… | QuickOSM | Install
Add a layer
  Zoom into the area (e.g. Canberra)
  Vector | QuickOSM | QuickOSM…
  Key = natural, Value = water
  In: Canvas Extent
  Advanced: Multipolygons
  Run Query
Save as shape file
  Click the save icon next to the layer name
  Choose Format: ESRI Shapefile
  Save in a directory.
    Will create several files, including a *.shp
Manage and Install Plugins
NOTE: You must download a layer for each of the zoom views (“Canvas Extent”). Thus, layers outside the area will not be retrieved. Trying to get the layer for the whole world will result in a timeout error.
Next: Add a Water Layer

## Slide 10
Add Layers
STEPS
Add a map layer. This must always be the last item in the Layers panel.
  Browser | XYZ Tiles | OpenStreetMap
Zoom in to a small region (e.g. Canberra)
Add a water layer
  Layer | Data Source Manager | Vector | File | Vector Datasets
  Open a saved shape file (* See slide #n for saving a file)
Change layer color
  Double click on the layer name (e.g. avs_water)
  Symbology | Color or pick from displayed colors
Next: Scale-based Visibility
 Right-click

## Slide 11
Sometimes you will find that a layer is not suitable for a given scale. For example, a dataset of all the continents may have low detail, and not be very accurate at street level. When that happens, you want to be able to hide the dataset at inappropriate scales. By setting a minimum scale for visibility, a layer will be masked when the zoom level is lower.
The water layer will disappear when the zoom level is above 100,000.
Scale-based Visibility
 Right-click
The GEOGLAM layer will only be visible at zoom levels above 4,000,000
Next: Attribute Data and Labelling

## Slide 12
All the objects that are visible on the map also have attributes. Maps in a GIS aren’t just pictures. They represent not only objects in locations, but also information about those objects. [Ref] The attribute data has info like ID, name, type, etc. for each feature. e.g. Lake Burley Griffin. These can be added to the map for clarity and information.
Attribute Data and Labelling
STEPS
View the attributes
  Select the layer
  Click the ‘Open Attribute Table” or F6
Add Labels from the attributes
  Select the layer
  Click the “abc” icon in the Label Toolbar and again on the window
  Choose ‘Single Lables”
  Choose “abs Name” under “Label With”
  Choose a color under “Stroke Color”
Edit labels
  Bring up the attributes table as in (1)
  Click the edit icon and type in the changes
  Save
End of Slide Show

## Slide 13
Title
Next:

## Slide 14: Acknowledgements